## Slide 1: LPS-SHA1: Low Power and Simple Implementation of Secure Hashing Algorithm (SHA1)using VHDL Implemented on FPGA
Choi Tim Antony Yung, Laurice Sattouf, Dimitri Garcia, Mohamed El-Hadedy Department of Electrical and Computer Engineering College of Engineering, California Polytechnic State University, Pomona Pomona, California
Email: {choiyung, lsattouf, dimitrig, mealy}@cpp.edu

## Slide 2: SHA1: Introduction
Hash Secure Algorithm (SHA1) is a cryptographic hash function which takes an input and produces a 160- bit hash value known as a message digest – typically rendered as a hexadecimal number, 40 digits long. It was designed by the untitled Sates National Security Agency.
Properties of SHA1: summarized in Table 1.
Algorithm | Message Size (bits) | Block Size (bits) | Word Size (bits) | Message Digest size (bits)
SHA1 | < 264 | 512 | 32 | 160
Table 1. Properties of secure Hash Function

## Slide 3: Motivation and Target:
Although SHA1 is Broken Algorithm in Cryptography, but it is still used as part of other hash based cryptography schemes. Therefore, in this presentation:
SHA-1 hash function is explored in depth and various implementations that have been proposed in the international literature are considered.
A system is presented to feed message as byte stream from a computer via UART to a Digilent Nexys A7 development board and display resulting SHA1 digest by VGA output.
Design aspects of performance and power dissipation are considered to explore and compare current implementations.

## Slide 4: Parameters and Operations used in SHA1 Algorithm
Federal Information (nist.gov)

## Slide 5: SHA1: Stages for SHA1 Algorithm
Preprocessing
  Padding the Message M.
  Parsing the message into message blocks.
  Setting the initial hash values
Hash Computation
(PDF) Design of a proven correct SHA circuit (researchgate.net)
Figure1. SHA1 algorithm steps

## Slide 6: Preprocessing
Includes three different steps:
Padding the message M:
  M is concatenated by bit 1, followed by k bits 0, followed by the 64-bit binary representation of number L.
  k is the least non-negative solution to the equation:
  (L+1+k) mod 512 = 448.
  The result is that the padded message is a multiple of 512.
Parsing the message into message blocks:
The message and its padding are parsed into N 512-bit blocks, M(1), M(2),…, M(N).
3) Setting the initial hash value, H(0):
the initial hash value, H(0), shall consist of the following five 32-bit words, in hex:
H(0) = 67452301
H(1) = efcdab89
H(2) = 98badcfe
H(3) = 10325476
H(4) = c3d2e1f0

## Slide 7: Hash computation:
SHA-1 uses a sequence of logical functions, f0, f1…f79. Each function ft, where 0 ≤ t ≤ 79, operates on three 32-bit words, x, y, and z, and produces a 32-bit word as output. The function ft (x, y, z) is defined as follows:
ft (x,y,z) = {
  Ch (x, y, z) = (x ∧ y) ⊕ ( ¬ x ∧ z) 0 ≤ t ≤ 19
  Parity (x, y, z) =x ⊕ y ⊕ z 20 ≤ t ≤ 39
  Maj (x, y, z) = (x ∧ y) ⊕ (x ∧ z) ⊕ (y ∧ z) 40 ≤ t ≤ 59
  Parity (x, y, z) = x ⊕ y ⊕ z 60 ≤ t ≤ 79
SHA-1 uses a sequence of eighty constant 32-bit words, K0, K1, …, K79, which are given by
Kt= { 5a827999 0 ≤ t ≤ 19
6ed9eba1 20 ≤ t ≤ 39
8f1bbcdc 40 ≤ t ≤ 59
ca62c1d6 60 ≤ t ≤ 79
Using these functions and constants, each message block, M(1) , M(2), …, M(N), is processed in order, using the following steps for i=0 to N
  1- Preparing the Message schedular:
Wt = { Mt(i) 0 ≤ t ≤15
ROTL1(Wt-3⊕Wt-8⊕Wt-14⊕Wt-16) 16≤t≤79
  2- Initialize the five working variables, a, b, c, d, and e, with the (i-1)st hash value:
a= H0(i-1)
b= H1(i-1)
c= H2(i-1)
d= H3(i-1)
e= H4(i-1)
  3- For t=0 to 79:
{
T= ROTL5 (a)+ ft(b, c, d)+e+ Kt +Wt
e=d
d=c
c=ROTL30 (b)
b=a
a=T
}
  4- Compute the ith intermediate hash value H(i):
H0(i) =a+ H0(i-1)
H1(i) =a+ H1(i-1)
H2(i) =a+ H2(i-1)
H3(i) =a+ H3(i-1)
H4(i) =a+ H4(i-1)
The steps will be repeated N time results a160-bit message digest of message M as follow:
H0(N) || H1(N) || H2(N) || H3(N) || H4(N)

## Slide 8: Architecture of SHA1 Operation Blocks
This is the architecture of the SHA1 core algorithm as a visual aid for all the previous steps.
Figure 2. Architecture of SHA1 Operation Blocks

## Slide 9: Implementation
Figure 3. Schematic of the implemented design of SHA1 Algorithm
7-Segment Dissplay
VGA communication Portocol
SHA-1 Core
UART Communication protocol
Clock divider component

## Slide 10: Results and Analysis
Figure 4. Screenshot of SHA-1 proposed design implementation results
Figure 5. Screenshot of SHA-1 [10] results

## Slide 11: Comparison
The integration of byte to word conversion circuit and specialization of performing SHA1 may contribute to the reduced LUTs and Flip-Flops used in this design comparing to a multifunctional design.
There is room for improvement on power consumption for this design.
  As Wt are generated by a combinational circuit, a possible improvement is to limit transition of signal on that logic to reduce power consumption, either by converting it to a sequential circuit or mask the activity of the circuit with an enable signal possibly from states signals to reduce signal transitions during idle states.
Algorithm | Power Consumption | LUT used | Flip Flops
[10] | 0.219 | 1171 | 1034
Proposed Design | 0.222 | 727 | 816
Table 2. Comparing Results of SHA-1 Implementations

## Slide 12: Conclusion
A hardware SHA1 digest core designed to reduce power consumption and resource usage was successfully implemented at register-transfer level by integrating byte to word conversion circuitry and eliminating usage of division circuit by separating message schedule counter into a 2-bit and 5-bit counters. A companion system was designed and implemented to handle serial byte stream message input via UART and output the resulting SHA1 digest to a VGA display. Future work includes further reduction of power consumption possibly by reducing idle state signal transitions.

## Slide 13: Demonstration:
Here is the link for our demonstration:
https://youtu.be/TPyGIwrq_no